## Slide 1: ESPNOW
Proprietary protocol developed by Espressif
ESP communication over Wifi band
Device Peering using MAC address
Limited to 250 bytes
Low power
Theoretical range of 400/500m in open air
Security: Peering and optional encryption using PSK

## Slide 2: Test setup
ESP32-C6-WROOM
Sensor
ESP32
Gateway
+ Externe Ethernet
ESPNOW
AWS IoT
MQTTS
EC2
API
InfluxDB
Grafana
HTTPS

## Slide 3: Test setup

## Slide 4: Software
Sensor
Configure as Wifi Station
Enable ESPNOW
Peer with gateway using the gateway MAC address
Send data
Deep sleep
Gateway
Configure as Wifi Access Point
Enable ESPNOW
Define callback function on message receive
In callback, send data to AWS IoT

## Slide 5: Results
Average current consumption in deep sleep: 205µA
Max current consumption while sending data: 63,4mA
Max current consumption while sending long distance: 110mA
Real world distance: about 10m indoors (multiple walls)
Time to send 117 bytes of data: +- 850ms
Deep sleep
+- 205µA
5 sec
Wifi setup and peering
+- 35 mA
0,6 sec
Sending data
+- 63 mA
0,25 sec

## Slide 6: Compared to wifi
Current consumption in deep sleep is similar
Current consumption in power on is about 20mA higher
Large difference in time to setup Wifi +-6 sec